## Slide 1: Janus – Evasion car
Cesar Galan

## Slide 2: Background
Tesla’s autonomous car cannot detect stationary objects at high speeds
I wanted to find a solution to this problem using sonar sensors
Later found out, Tesla went around this problem by adding a sonar sensor in front of the car and two to the sides

## Slide 3: Project Overview
Goals:
Control the speed of a car as it approaches an obstacle
Stop the car at some distance from the wall
Car needs to go at full speed when there is not a wall
Strategy:
Use an ultrasonic sensor to identify the distance from an obstacle
Control the speed of the car by changing the PWM signal into the motor driver

## Slide 4: Hardware
Part Name | Source | Specs
Ultrasonic sensor HC-SR04 | Gear Best | Distance detection: 2cm – 450cm ± .3cm Sensor Angle: 15 degrees Voltage output: 5V at 2mA
29:1 Metal Gearmotor #1162 | Trudy’s shop/ Pololu | No load Speed @ 6: 450 RPM No-Load Current @6: 250 mA Stall Torque @6: 25 oz-in
DRV8838 Single Brushed DC Motor Driver Carrier | Pololu | Motor supply voltage: 0V – 11V Logic supply voltage: 1.8V – 7V PHASE/ENABLE interface to control direction and speed
Breadboard | Sparkfun | -
Pillow block bearing | McMaster | Max Speed: 56000 RPM
Acrylic | Laser Cutter room | -
Wheels and shaft | Goodwill | -

## Slide 5: System block diagram
Ultrasonic sensor: Reads the distance
PIC18: Computes the power based on error and displays the variables
Motor driver: Controls the output current into DC motor
DC Motor: Controls the speed of the car

## Slide 6: Circuit diagram
RC2: Controls the motor speed
RE0: Turns the motor on and off
RE1: Triggers the sonic sensor
RD4: Reads when the signal is back

## Slide 7: Software
Initialization: Initialize all of the pins and LCD as well as dummy variables
Measure distance: Find the distance from the wall
Calculate power: Computes error and uses control law to find the output power
Outputs PWM signal: Interrupts on compare CCP1 to enter the low priority interrupt

## Slide 8: Final product

## Slide 9: Lessons Learned
Problems:
Interfacing: Gear alignment
CCP1 falling behind the timer1
PWM signal not working for values other than 50%
Going from error to power into the motor
Solutions:
Apoxy the motor prevent vibrations at low speeds
Not adding the correct amount to the CCP extension
Scale the control to the max error over max power

## Slide 10: Final Product performance
Needs above 50% PWM signal in order for the car to overcome weight
The code cap the max power to be 90%
Proportional gain was found to be around 2
Car does not move fast enough to implement PI or PD control
  though it is incorporated into the code

## Slide 11: Thanks
Trudy: Guiding me on the construction of the car
Devon and Lewis: For debugging my code over and over
Codie: For letting me borrow the phone charger
Grant: For the Velcro and 9 volt battery

## Slide 12: Questions?